## Slide 1
2021.11.11
彭天祥

## Slide 2
一个示例程序

## Slide 3
一个示例程序
这意味着
- CPU是多发射的
- CPU在运行时对指令进行了动态调度，乱序执行

## Slide 4
一个示例程序
imul %eax, %eax
imul %eax, %eax
…
imul %edx, %edx
imul %eax, %eax
…
第二个imul指令的执行依赖于前一个imul指令的结果，造成了数据依赖
RAW

## Slide 5
Register & Memory Location Dependence
- 只存在相同reg/mem之间
- 通过相同reg/mem流通

## Slide 6
Register & Memory Location Dependence
- 分为：
- data dependence: RAW(Read After Write)
■ addi x1, x1, -8
■ bne x1, x2, Loop
- name dependence(never happen if we have infinite registers)
- anti-dependence: WAR(Write After Read)
■ fadd.d f4, f0, f2
■ fld f0, 0(x1)
- output dependence: WAW(Write After Write)
■ addi x1, x4, x5
■ addi x2, x1, -8
■ addi x1, x7, x8
- not dependence
- RAR(Read After Read)
RAW
WAR
WAW

## Slide 7
Register & Memory Location Dependence
依赖产生的方式：reg vs. mem（以RAW为例）
- 通过访问相同reg产生
- reg reg
■ addi x1, x1, -8
■ bne x1, x2, Loop
- mem reg
■ fld f0, 0(x1)
■ fadd.d f4, f0, f2
- reg mem
■ fadd.d f4, f0, f2
■ fsd f4, 0(x1)

## Slide 8
Register & Memory Location Dependence
依赖产生的方式：reg vs. mem（以RAW为例）
- 通过访问相同mem产生
- mem mem
    ■ fsd f4, 0(x1)
    ■ fld f2, 0(x1)

## Slide 9
Register & Memory Location Dependence
依赖产生的方式：reg vs. mem
- WAW & WAR类似，无法确保依赖意味着即使是单核，程序的正确性也会丧失
- 由什么指令（mem access、reg operation）产生不重要（reg的三种方式都一样）
- 重要的是媒介是reg还是mem：为什么？

## Slide 10
Register & Memory Location Dependence
RAR：not dependence
- mem reg
■ fsd f0, 0(x1)
■ fadd.d f2, f0, f4
- reg mem
■ fadd.d f2, f0, f4
■ fsd f0, 0(x1)
- reg reg
■ addi x2, x1, x4
■ addi x3, x1, x5
- mem mem
■ fld f0, 0(x1)
■ fld f2, 0(x1)

## Slide 11
Register & Memory Location Dependence
RAR：not dependence
- mem mem
■ fld f0, 0(x1)
■ fld f2, 0(x1)
- 单核：任意乱序，不影响程序正确性

## Slide 12
Register & Memory Location Dependence
RAR：not dependence
- mem mem
■ fld f0, 0(x1)
■ fld f2, 0(x1)
- 多核：
program order：
■ fld f0, 0(x1)
    ■ fld f2, 0(x1)
reordered（static/dynamic）：
■ fld f2, 0(x1)
    ■ fld f0, 0(x1)
initial：mem[x1] = 0
---------another core writes mem[x1] = 1 ---------
f0 = 0, f2 = 1
f2 = 1, f0 = 0
Memory Consistency

## Slide 13
Register & Memory Location Dependence
依赖产生的方式：reg vs. mem
- 差异：可见性
- 因为reg对外不可见，所以：
- 维护RAW、WAW、WAR是为了维护程序的正确性
- RAR不是一种依赖
- 因为mem对外可见，所以：
- 维护RAW、WAW、WAR依赖是为了维护程序的正确性，同时
在多核情景下维护了memory consistency
- 维护RAR是为了维护memory consistency
- 如果能确保reorder不会被观测到（从而对外部造成影响），可以
对RAR乱序（consistency speculation）

## Slide 14
Hazard
Dependence一定会导致程序执行错误吗？
以五级流水线为例
■ addi x1, x1, -8
■ subi x2, x7, 2
■ sd x2, -12(x3)
■ ld x7, -16(x3)
■ addi x7, x7, -8
■ bne x1, x2, Loop
RAW
■ addi x1, x1, -8
■ bne x1, x2, Loop
■ subi x2, x7, 2
■ sd x2, -12(x3)
■ ld x7, -16(x3)
■ addi x7, x7, -8
RAW
not hazard
hazard：overlapping of execution

## Slide 15
Hazard
Eliminate Hazard(in-order pipeline)
- RAW
- RAW from calculation：forwarding
■ addi x1, x1, -8
■ bne x1, x2, Loop
- RAW from memory access：stall
■ ld x1, 0(x2)
■ addi x1, x1, -8

## Slide 16
Hazard
Eliminate Hazard(in-order pipeline)
- WAW & WAR & RAR
- never happen(due to in-order execution)
- Most hazards arise from out-of-order execution

## Slide 17
Hazard
Eliminate Hazard(in-order pipeline)
- WAW & WAR & RAR
- never happen(due to in-order execution)
Most hazards arise from out-of-order execution

## Slide 18
Sequential Consistency
（r1，r2）=（0，？）
（r1，r2）=（SET，NEW）

## Slide 19
Sequential Consistency
L2
---------------
S1
---------------
S2
---------------
L1
（r1，r2）=（SET，0）
Load-Load reorder

## Slide 20
Sequential Consistency
S2
---------------
L1
---------------
L2
---------------
S1
（r1，r2）=（SET，0）
Store-Store reorder

## Slide 21
Sequential Consistency
SC：
permits（0，？），（SET，NEW）
forbids（SET，0）

## Slide 22
Sequential Consistency
SC requires:
Program order vs. Memory order

## Slide 23
Sequential Consistency
SC requires:
Program order vs. Memory order

## Slide 24
Sequential Consistency
Constraints:
S1 <m S2
L1 <m L2
Legal orders:
A(4, 4) / (2 * A(2, 2)) = 6

## Slide 25
Sequential Consistency
L2
---------------
S1
---------------
S2
---------------
L1
volatile:
L1 <p L2 => L1 <m L2
（r1，r2）=（SET，0）
Load-Load reorder

## Slide 26
Sequential Consistency
S2
---------------
L1
---------------
L2
---------------
S1
volatile:
S1 <p S2 => S1 <m S2
（r1，r2）=（SET，0）
Store-Store reorder

## Slide 27
Sequential Consistency
In Summary

## Slide 28
Sequential Consistency
Naïve Implementation: Multi-tasking Uniprocessor
1. On a context switch, any pending memory operations must be completed before switching to the new thread
2. Correctly honors memory dependencies
- all of the SC rules are enforced

## Slide 29
Sequential Consistency
Naïve Implementation: The Switch
1. Program-order request: Each core Ci seeks to do its next memory access in its program order <p. Each core can use any optimizations that do not aﬀect the order in which it presents memory operations to the switch.
2. Program-order completion: The switch selects one core, allows it to complete one memory access, and repeats; this deﬁnes memory order <m.
No cache, each memory access instruction initiates a request.

## Slide 30
Sequential Consistency
Implementation with
Cache-Coherence System
1. Program-order request: Each core Ci seeks to do its next memory access in its program order <p. Each core can use any optimizations that do not aﬀect the order in which it presents memory operations to the switch.
2. Program-order completion: The memory system selects one core, allows it to complete one memory access, and repeats; this deﬁnes memory order <m.
Before cache, each memory access instruction initiates a request.

## Slide 31
Sequential Consistency
Implementation with L1-cache
Cache-Coherence System
1. Program-order request: …
2. Program-order completion: the memory system can respond to requests from diﬀerent cores in parallel, provided that the corresponding L1 caches have the appropriate permissions. Completions may be placed into memory order in any logical order.
Before cache, each memory access instruction initiates a request.

## Slide 32
Sequential Consistency
Implementation with L1-cache
Cache-Coherence System

## Slide 33
Out-of-Order
为什么会发生乱序？
编译器：static scheduling
CPU：dynamic scheduling

## Slide 34
Out-of-Order: Compiler
- Motivation: two typical compiler optimizations
- Optimization goals & principles
- Problems & Solutions

## Slide 35
Out-of-Order: Compiler
Motivation: two typical compiler optimizations
- Static Register Renaming
- Filling Stall

## Slide 36
Out-of-Order: Compiler
Example：Static Register Renaming
Latency: addf - 3 cycles, mulf - 6 cycles, divf - 24 cycles
■ addf f0, f1, f2
■ mulf f3, f0, f2
■ addf f4, f3, f2
■ mulf f5, f4, f2
■ divf f5, f1, f2
RAW
RAW
RAW
WAW
■ addf f0, f1, f2
■ mulf f3, f0, f2
■ addf f4, f3, f2
■ mulf f5, f4, f2
■ divf f6, f1, f2

## Slide 37
Out-of-Order: Compiler
Example：Filling Stall
8 cycles per loop element(assume bne 0 latency from predictor)

## Slide 38
Out-of-Order: Compiler
Example：Filling Stall
8 cycles per loop element(assume bne 0 latency from predictor)

## Slide 39
Out-of-Order: Compiler
Example：Filling Stall
8 vs. 7 cycles per loop element
Before:
After:

## Slide 40
Out-of-Order: Compiler
Example：Filling Stall
8 vs. 3.5 cycles per loop element
Before:
After:

## Slide 41
Out-of-Order: Compiler
Optimization goals & principles
- Register Renaming：
-（尽可能）消除name dependence（WAW、WAR）
- 因为并不是真正的依赖，只是因为我们资源不足
- Filling Stall：
- 对register：维持data dependence（RAR）以及可能的name dependence，尽可能
消除部件冲突带来的Stall（浮点mul、div）
- 对memory：
- 不同地址：默认假设没有依赖，随意乱序，掩盖访存延迟（cache hit、cache miss）
- 相同地址：禁止重排 => 保证单线程下的sequentiality
为什么会发生对相同地址的Load-Load？
- 默认具有不变性
- volatile variable
- 寄存器压力（多余的值通过访问栈、共享变量进行）

## Slide 42
Out-of-Order: Compiler
Problems & Solutions: spinlock

## Slide 43
Out-of-Order: Compiler
禁止编译器重排
Problems & Solutions: spinlock

## Slide 44
Out-of-Order: Compiler
Core1：
L1：check other refs
L2：check dirty
Core2：
S2：mark dirty
S1：release ref
other refs & clean/dirty => cannot_free
no other refs & dirty => cannot_free
no other refs & clean => free
Problems & Solutions: spinlock

## Slide 45
Out-of-Order: Compiler
Core1（Reordered）：
L2：check dirty
L1：check other refs
Core2：
S2：mark dirty
S1：release ref
L2 -> S2 -> S1 -> L1
no other refs & dirty => free!
Prevent compiler/CPU from reordering Load-Load
Problems & Solutions: remove_mapping

## Slide 46
Out-of-Order: Compiler
x86 employs TSO model, inherently forbidding Load-Load reordering, so compiler barrier is just enough.
Problems & Solutions: remove_mapping

## Slide 47
Out-of-Order: CPU
- Motivation: reduce structural(stage) conflict
- Dynamic Scheduling: eliminate stalls from stage conflict
- Register Renaming: eliminate WAW/WAR dependence
- Speculation: reduce control dependence
- In Summary: Out-of-Order CPU execution model

## Slide 48
Motivation: reduce structural(stage) conflict
Basic five-stage pipeline

## Slide 49
Motivation: reduce structural(stage) conflict
Basic five-stage pipeline

## Slide 50
Motivation: reduce structural(stage) conflict
Problems for FP operations:
- Finish FP add/mul/div in single cycle
- High propagation delay => low clock frequency
- Finish FP add/mul/div in multiple cycles
- FP operations will block later instructions for a long time

## Slide 51
Motivation: reduce structural(stage) conflict
Extend pipeline for multi-cycles FP operations

## Slide 52
Motivation: reduce structural(stage) conflict
Extend pipeline for multi-cycles FP operations
At most
- one outstanding integer execution/memory access
- seven outstanding FP/integer multiplies
- four outstanding FP adds
- one outstanding FP divide

## Slide 53
Motivation: reduce structural(stage) conflict
Extend pipeline for multi-cycles FP operations
New problems
- register write port conflict
- WAW hazard

## Slide 54
Motivation: reduce structural(stage) conflict
Extend pipeline for multi-cycles FP operations
may arrive write-back stage at the same cycle
New problems: register write port conflict

## Slide 55
Motivation: reduce structural(stage) conflict
Extend pipeline for multi-cycles FP operations
New problems: register write port conflict
Solution:
(1) Detect at ID stage, stall
(2) Detect before write-back stage, stall
- will propagate to the whole pipeline

## Slide 56
Motivation: reduce structural(stage) conflict
Extend pipeline for multi-cycles FP operations
New problems: WAW hazard
Solution:
(1) Detect at ID stage, stall
(2) Stamp out result of earlier write as NOP at write-back stage
- no impact on RAW forwarding at the end of execution stage
WAW

## Slide 57
Motivation: reduce structural(stage) conflict
Extend pipeline for multi-cycles FP operations
In summary
- in-order issue
- in-order execution
- completion：
- in-order for Integer(memory access in order)
- out-of-order for FP

## Slide 58
Motivation: reduce structural(stage) conflict
Extend pipeline for multi-cycles FP operations
Stall & Hazards preventing from starting execution
- RAW Hazard Detect
- Structural Conflict
- e.g. divide
- register write port
- WAW Hazard Detect
- Stage Conflict
Is WAR possible?
- No. Guaranteed by in-order execution.
■ fmul.d f1, f2, f4
■ fadd.d f4, f0, f2

## Slide 59
Dynamic Scheduling: eliminate stalls from stage conflict
Motivation: eliminate stage conflict
■ fadd.d f2, f0, f1
■ fmul.d f4, f2, f3
■ fsub.d f7, f0, f1
RAW
fmul.d stalls for RAW hazard
fsub.d stalls for fmul.d stalling

## Slide 60
Simple dynamic scheduling with Scoreboarding technique
Scheduling later instructions into execution if earlier instructions stall
Requires two main changes:
- additional FIFO instruction queue at IF stage
- WAR hazard detect
Dynamic Scheduling: eliminate stalls from stage conflict

## Slide 61
Simple dynamic scheduling with Scoreboarding technique
New problem: WAR hazard
■ fdiv.d f2, f0, f1
■ fmul.d f4, f2, f3
■ fadd.d f3, f0, f1
RAW
WAR
WAR detect & stall
Dynamic Scheduling: eliminate stalls from stage conflict

## Slide 62
Simple dynamic scheduling with Scoreboarding technique
In summary
- in-order issue
- out-of-order execution
- completion：
- in-order for Integer(memory access in order)
- out-of-order for FP
Dynamic Scheduling: eliminate stalls from stage conflict

## Slide 63
Simple dynamic scheduling with Scoreboarding technique
Consider:
- RAW/WAW Hazard Detect at ID stage
- Dynamic Scheduling at ID stage
- Structural Conflict
- e.g. divide
- register write port
- Stage Conflict
- WAR Hazard Detect at WB stage
Dynamic Scheduling: eliminate stalls from stage conflict

## Slide 64
Register Renaming: eliminate WAW/WAR dependence
Motivation: eliminate WAW/WAR dependence
- RAW/WAW Hazard Detect at ID stage
- Dynamic Scheduling at ID stage
- Structural Conflict
- e.g. divide
- register write port
- WAR Hazard Detect at WB stage
Not exist if we have infinite registers

## Slide 65
Out-of-Order: CPU
Instruction Queue
Issue Stage
Reorder Buffer
FU
FU
…
Register File
Cache Coherence System
Local Cache
in-order issue
out-of-order execution
in-order
commit

## Slide 66
Sequential Consistency
Problem of speculation
Issue Stage
Reorder Buffer
Local Cache
issue Load 1

## Slide 67
Sequential Consistency
Problem of speculation
Issue Stage
Reorder Buffer
Not ready: Load 1 cache miss
issue Load 2
Local Cache

## Slide 68
Sequential Consistency
Problem of speculation
Issue Stage
Reorder Buffer
Not ready: Load 1 cache miss
Ready: Load 2 cache hit: 0
Local Cache

## Slide 69
Sequential Consistency
Problem of speculation
Issue Stage
Reorder Buffer
Not ready: Load 1 cache miss
Ready: Load 2 cache hit: 0
Local Cache
Store 1: data = NEW
Store 2: flag = SET

## Slide 70
Sequential Consistency
Problem of speculation
Issue Stage
Reorder Buffer
Ready: Load 1 cache hit: SET
Ready: Load 2 cache hit: 0
Local Cache
Store 1: data = NEW
Store 2: flag = SET

## Slide 71
Sequential Consistency
Problem of speculation
Issue Stage
Reorder Buffer
Ready: Load 2 cache hit: 0
Local Cache
Store 1: data = NEW
Store 2: flag = SET
commit Load 1: SET

## Slide 72
Sequential Consistency
Problem of speculation
Issue Stage
Reorder Buffer
Local Cache
Store 1: data = NEW
Store 2: flag = SET
commit Load 1: SET
commit Load 2: 0

## Slide 73
Sequential Consistency
Non-binding prefetch
Issue Stage
Reorder Buffer
Not ready: Load 1 cache miss
issue Load 2
Local Cache

## Slide 74
Sequential Consistency
Issue Stage
Reorder Buffer
Not ready: Load 1 cache miss
Not Ready: Load 2 prefetch
Local Cache
Non-binding prefetch

## Slide 75
Sequential Consistency
Issue Stage
Reorder Buffer
Ready: Load 1 cache hit: SET
Local Cache
Store 1: data = NEW
Store 2: flag = SET
Not Ready: Load 2 prefetch
Non-binding prefetch

## Slide 76
Sequential Consistency
Issue Stage
Reorder Buffer
Local Cache
Store 1: data = NEW
Store 2: flag = SET
commit Load 1: SET
Not ready: Load 2 cache miss
Non-binding prefetch

## Slide 77
Sequential Consistency
Issue Stage
Reorder Buffer
Local Cache
Store 1: data = NEW
Store 2: flag = SET
commit Load 1: SET
Ready: Load 2 cache hit: NEW
Non-binding prefetch

## Slide 78
Sequential Consistency
Issue Stage
Reorder Buffer
Local Cache
Store 1: data = NEW
Store 2: flag = SET
commit Load 1: SET
commit Load 2: NEW
Non-binding prefetch

## Slide 79
Sequential Consistency
Implementing Atomic RMW(Read-Modify-Write) Instructions
e.g.
1. fetch and increment - atomic add
2. atomic swap - xchg
3. compare and swap - cmpxchg

## Slide 80
Sequential Consistency
Implementing Atomic
Instructions
1. Naïve implementation: Lock memory system
- prevent other cores from issuing memory accesses
- perform read-modify-write to memory
- unnecessary performance loss

## Slide 81
Sequential Consistency
Implementing Atomic
Instructions
2. Exclusive cache ownership
- first obtain block RW ownership in its local cache
- local cache waits to service any incoming coherence request for the block until after the store

## Slide 82
Sequential Consistency
Implementing Atomic
Instructions
3. Speculative execution
- Initially local cache owns read-only block
- load part: speculatively request RW ownership
- store part: first check local cache invalidation:
- still valid(which means RW): perform store immediately
- invalid: mis-speculation SC, reissue and execute

## Slide 83
Total Store Order Consistency
Motivation: avoid stall Load after Store
- Because stores are common, being able to avoid stalling on most of them is an important beneﬁt.
- Moreover, it seems sensible to not stall the core because the core does not need anything, as the store seeks to update memory but not core state.
L(a) L(a)
L(b) S(b)
S(a) S(a)
S(b) L(b)

## Slide 84
Instruction Queue
Issue Stage
Reorder Buffer
FU
FU
…
Register File
Cache Coherence System
Local Cache
in-order issue
out-of-order execution
in-order
commit
(FIFO)
Store
Buffer
Store into store buffer after commit.
Later Load may commit bypass earlier stores(before them drain to cache).
Total Store Order Consistency

## Slide 85
For uniprocessor:
L-L/L-S remains ordered through ROB, /S-S remains ordered through Write Buffer
S(a)-L(b) reorder is not invisible i.e. execution appears to be SC
S(a)-L(a) reorder introduces RAW hazard, volatiles SC => local bypass from store buffer => execution appears to be SC
Total Store Order Consistency

## Slide 86
When building a multicore processor, it seems natural to use multiple cores, each with its own bypassing write buﬀer, and assume that the write buﬀers continue to be architecturally invisible.
Total Store Order Consistency

## Slide 87
This assumption is wrong.
Total Store Order Consistency

## Slide 88
According to SC, (r1, r2) = (0, 0) should never happens, because:
result implies: L1 <m S2 & L2 <m S1
program order: S1 <p L1 & S2 <p L2
chained: S1 <p L1 <m S2 <p L2 <m S1
Total Store Order Consistency
1

## Slide 89
This may happen on multiprocessor system with their own bypassing write buffers.
How?
Total Store Order Consistency
1

## Slide 90
Total Store Order Consistency
Issue Stage
ROB
(FIFO)
Store
Buffer
1
L1
S1
ready
issue
cache miss
Issue Stage
ROB
(FIFO)
Store
Buffer
L2
S2
Core1
Core2

## Slide 91
Total Store Order Consistency
Issue Stage
ROB
ready
issue
(FIFO)
Store
Buffer
1
L1
S1
cache miss
Issue Stage
ROB
(FIFO)
Store
Buffer
L2
S2
Core1
Core2

## Slide 92
Total Store Order Consistency
Issue Stage
ROB
(FIFO)
Store
Buffer
1
S1
commit: r1 = 0
ready
issue
cache miss
Issue Stage
ROB
(FIFO)
Store
Buffer
S2
commit: r2 = 0
Core1
Core2

## Slide 93
Total Store Order Consistency
Issue Stage
ROB
(FIFO)
Store
Buffer
1
S1
commit: r1 = 0
ready
issue
cache miss
Issue Stage
ROB
(FIFO)
Store
Buffer
S2
commit: r2 = 0
Core1
Core2

## Slide 94
Total Store Order Consistency
Issue Stage
ROB
(FIFO)
Store
Buffer
1
commit: r1 = 0
ready
issue
cache miss
Issue Stage
ROB
(FIFO)
Store
Buffer
commit: r2 = 0
commit: x = NEW
commit: y = NEW
Core1
Core2

## Slide 95
Without write buﬀers, the hardware is SC, but with write buﬀers, it is not, making write buﬀers architecturally visible in a multicore processor.
- To hold SC: turn it off => potential performance impact
- To abandon SC: (r1, r2) = (0, 0) is permitted => TSO
Total Store Order Consistency
1

## Slide 96
Total Store Order Consistency
TSO requires:

## Slide 97
Total Store Order Consistency
TSO requires:

## Slide 98
Total Store Order Consistency
TSO requires:

## Slide 99
Total Store Order Consistency
TSO requires:

## Slide 100
Total Store Order Consistency
In Summary

## Slide 101
Total Store Order Consistency
Naïve Implementation:
The Switch
1. Loads and stores leave each core in that core’s program order <p.
2. A load either bypasses a value from the write buﬀer or awaits the switch as before.
3. A store enters the tail of the FIFO write buﬀer or stalls the core if the buﬀer is full.
4. When the switch selects core Ci, it performs either the next load or the store at the head of the write buﬀer.

## Slide 102
Total Store Order Consistency
1. Loads and stores leave each core in that core’s program order <p.
2. A load either bypasses a value from the write buﬀer or awaits the switch as before.
3. A store enters the tail of the FIFO write buﬀer or stalls the core if the buﬀer is full.
4. When the switch selects core Ci, it performs either the next load or the store at the head of the write buﬀer.
Implementation with
Cache-Coherence System

## Slide 103
Total Store Order Consistency
Problem of speculation

## Slide 104
Total Store Order Consistency
Implementing Atomic
Instructions
Key difference:
- RMW are written to write buffer
- We have to drain the store buffer before starting a RMW
- Why?

## Slide 105
Total Store Order Consistency
Implementing Atomic
Instructions
View RMW as a load-store atomic instruction pair:
- load part never reorder with earlier load(TSO), guaranteed by ROB
- load part may reorder with earlier store(TSO) e.g. S0 in Store Buffer
- if load part reorders with earlier store, store part will also reorder with earlier store, which volatiles TSO
Issue Stage
ROB
(FIFO)
Store
Buffer
S0
Load part
Store part
RMW inst:
hold RW ownership

## Slide 106
Total Store Order Consistency
Implementing Atomic
Instructions
View RMW as a load-store atomic instruction pair:
- load part never reorder with earlier load(TSO), guaranteed by ROB
- load part may reorder with earlier store(TSO) e.g. S0 in Store Buffer
- if load part reorders with earlier store, store part will also reorder with earlier store, which volatiles TSO
- relinquishing RW ownership volatiles atomicity
Issue Stage
ROB
(FIFO)
Store
Buffer
S0
RMW inst:
release RW ownership, write into Write Buffer
RMW

## Slide 107
Total Store Order Consistency
Implementing Atomic
Instructions
View RMW as a load-store atomic instruction pair:
- drain store buffer before starting load part
Issue Stage
ROB
(FIFO)
Store
Buffer
S0
Load part
Store part
RMW inst:
hold RW ownership

## Slide 108
Total Store Order Consistency
Implementing Atomic
Instructions
View RMW as a load-store atomic instruction pair:
- drain store buffer before starting load part
- write into cache without relinquishing RW ownership
Issue Stage
ROB
(FIFO)
Store
Buffer
Load part
Store part
RMW inst:
hold RW ownership

## Slide 109
Total Store Order Consistency
Implementing Atomic
Instructions
View RMW as a load-store atomic instruction pair:
- drain store buffer before starting load part
- write into cache without relinquishing RW ownership
Issue Stage
ROB
(FIFO)
Store
Buffer
RMW inst:
hold RW ownership
RMW

## Slide 110
Total Store Order Consistency
Implementing Fence
Fence:
- reserve Store-Load order explicitly
- protecting Load from reordering with earlier Store is enough

## Slide 111
Total Store Order Consistency
Implementing Fence
Fence:
1. draining the write buﬀer when a FENCE is executed
2. not permitting subsequent loads to execute until an earlier FENCE has committed
Issue Stage
ROB
(FIFO)
Store
Buffer
S0
fence
load
Preparing operand(calculate effective address) and non-binding prefetch are permitted
Accessing memory(cache) is not permitted

## Slide 112
感谢观看
彭天祥